## Slide 1: Bridge Administration

## Slide 2: Bridge Classes
Class One – bridge handles large ocean going ship traffic. i.e. Tankers, container ships, LNG tankers, bulk carriers
Class Two - bridge handles smaller commercial and larger recreational boat traffic. Used by tugs & barges, but no ocean going vessels.

## Slide 3: Bridge Classes
Class Three – bridge handles recreational traffic only. No tugs or barges use this bridge regularly.
  Class Four - nothing but rowboats and small outboards move under this bridge.
    The C.G. is not interested in these. Do not survey unless specifically requested.
    Can represent up to 60 percent of total bridges in your AOR.

## Slide 4: Bridge Light Permit:

## Slide 8
Coast Pilot

## Slide 9
Light List

## Slide 10
Local Notice to Mariners

## Slide 11
ACOE chart

## Slide 12
ACOE chart

## Slide 13
33CFR117 regulations

## Slide 15: Bridge Lights:
Channel Center Lights G -360 
Channel Margin Lights R- 180
Pier Lights R- 180
Channel Axis Lights R- 180
Preferred Channel Lights 3W - 180 
Movable Span Lights
R > G - 180

## Slide 16: Bridge Lights:
LED Lanterns

## Slide 17: Bridge Lights:
Light Pipes
6” diameter tube illuminated from one end
Used in urban areas with high background lighting problems
Used for Channel Center Lights and Channel Margin Lights
Newer units going to LED lighting over full length

## Slide 18: Light Pipes:

## Slide 19
Channel Center Lights
(on Fixed Bridges)
  Two 360-degree lanterns, hang just under lip.
  Visible from both approach channels – up and down stream.
  Green in color.
  Lanterns should appear as range lights mounted under the lip of the bridge’s span.
  Mark the center of the navigable channel.

## Slide 20
Movable Span Lights
(on Movable Span Bridges – Draw Bridges)
180-degree split-lanterns facing toward the
traffic.
  Shows a RED light when the draw is closed
  or moving.
  Shows a GREEN light when the draw is open.

## Slide 21: Channel Axis Lights:
  180-degree lanterns that face the center of channel.
  RED in color.
  Mark any bends in the channel or turns in the pier structures on a bridge.

## Slide 22: Channel Margin Lights:
  180-degree lanterns that face into the traffic.
  RED in color.
  Mark the edges of the navigable channel.
  Are positioned above the lip of the span. These lights mark low steel - the lower limit of the span clearance.

## Slide 23: Channel Margin Lights
Lights define the limits of the navigable channel.

## Slide 24: Pier Lights:
180-degree lanterns – facing the traffic. RED in color. Mark the piers on the bridge. Note that they are used for a different purpose than Axis lights.

## Slide 25
Two Major Types of Bridges:
1. Fixed Bridges (1)
2. Movable Span or Draw Bridges (5)
  Lift Bridges
  Swing Bridges
  Bascule Bridges
      Single Bascule & Double Bascule
  Retractable Bridges

## Slide 26
Single Span Fixed Bridge
180° RED Channel Margin Lights
360° GREEN
Channel Center Lights
Appears as a range under the lip of the span.
Should be mounted just below the lip of the span.

## Slide 27
Multiple Channel Fixed Bridge

## Slide 28
Multiple Span Fixed Bridge
180° Red Pier & Margin Lights
360° Green Channel Center Lights
3 180° White
Preferred Channel Lights

## Slide 29
Single Span Swing Bridge - Closed

## Slide 30
Double Span Swing Bridge - Closed
Pivot
North Swing Span
South Swing Span
Coleman Memorial Bridge, Yorktown VA

## Slide 31
Swing Bridge - OPEN

## Slide 32
Swing Bridge – In Motion one navigable channel

## Slide 33
Swing Bridge - Closed
Moveable Span Lights -alternate Red & Green, each 60° at 90° to each other. Show RED when the bridge is closed.
180° Red Pier Lights

## Slide 34
Swing Bridge - Open
Moveable Span Lights-Alternate Red & Green, each 60° at 90° to each other.
180° Red Pier Lights

## Slide 35
Vertical Lift Bridge Closed

## Slide 36
Vertical Lift Bridge – Open Chart may show Hor CL and the open and closed Vert CL.

## Slide 37
Vertical Lift Bridge – Span is closed
180° Red Pier Lights
180° Red Moveable Span Light is on.
360° Green Moveable Span Light is Out

## Slide 38
Vertical Lift Bridge – Span is open
180° Red Pier Lights
180° Red Moveable Span Light is out
360° Green Moveable Span Light is on.

## Slide 40
Single Bascule Bridge Closed

## Slide 41
Double Span Bascule Bridge (closed)

## Slide 42
Bascule Bridge
Movable Span Light
Pier Lights

## Slide 43
Single Bascule Bridge – Span is closed
180° Red Pier Lights
180° Green Moveable Span Light is out.
180° Red Moveable Span Light is on.

## Slide 44
Single Bascule Bridge – Span is open
180° Green Moveable Span Light is on.
180° Red Moveable Span Light is out.
Draw must open to point where it clears the fenders

## Slide 45
Single Bascule Bridge – Span open

## Slide 46
Double Bascule Bridge
(Spans are closed)
180° Red Pier Lights
180° Green Moveable Span Light is out.
180° Red Moveable Span Light is on.

## Slide 47
Double Bascule Bridge (Spans are open)
180° Red Pier Lights
180° Green Moveable Span Light is on.
180° Red Moveable Span Light is out.

## Slide 48
Adjacent Double Bascule Bridge (Spans are closing)

## Slide 49
Lighting Discrepancies
Unlit
Broken Axis Light Lens
Flow Down River

## Slide 50: Navigational Lighting
ONLY GREEN LIGHT
SHOULD BE BELOW
LOW STEELOF BRIDGE

## Slide 51: Lighting Discrepancy

## Slide 52: Lighting Discrepancies
Lights extinguished / Dirty globe
Color and arc of visibility
Center of channel vs center of bridge location
Green center channel lights providing range (fixed bridges)
Red margin of channel lights no lower than low steel

## Slide 53: Wales – the horizontal wooden components of the fender system
Wales must be:
  In good repair.
  Have no sharp metal or bolts sticking into the channel.
  Have no metal corners.

## Slide 54
WALES

## Slide 55: Special Regulation Signs must be:
Readable.
Located on both sides of bridge.
Match the Federal Regulations for that bridge in the 33CFR117 Subpart B
If a phone is required to open a lift bridge, the phone number must be shown on the regulatory sign.

## Slide 56
Special Regulatory Signs

## Slide 57: Bridge Signage

## Slide 58: Fender Discrepancies:
Missing or broken wales
Fender protruding into channel
Steel/metal exposed to channel
Bolts not recessed
Dolphin clusters “leaning”
Broken or dirty vertical clearance gauge
Missing or inaccurate drawbridge operating regulatory sign
PHOTOS REQUESTED

## Slide 59: Bridge Fenders
PROTRUDING BOLTS
TOP VIEW
STEEL JACKETING

## Slide 60: Missing Wales

## Slide 61: Fender Damage Spuyten-Duyvil RR

## Slide 62: Bridge Fenders
PROTRUDING BOLTS
MISSING WALES

## Slide 63: Protective Piers must be:
Wrapped with steel cable.
Have nothing projecting into the navigable channel.
Undamaged
Not be rotting at the waterline.
Not be rotting down from the top.

## Slide 64: Damaged Cell

## Slide 65: Leaning Submerged Cluster

## Slide 66: Protruding Wales

## Slide 67: Clearance Gauges
May be required on both Fixed Bridges and Draw Bridges:
Required only if specified on CG Bridge permit
May be listed in 33CFR117 -Subpart B (may still be required by permit, even if not listed in 33CFR117)
Listing is also found in the Coast Pilot

## Slide 68
CLEARANCE GAUGES
Clearance gauges are not always required but may be found on many Bridges. Check 33CFR117 or the Coast Pilot

## Slide 69: Clearance Gauges
Should be mounted on the right side of the channel on both sides of the bridge (upstream & downstream).
Should be readable from ½ mile.
Must reflect the actual clearance from the lowest point of the span over the navigable channel to the actual water surface.

## Slide 70: Clearance Gauges

## Slide 71: Broken Gauge

## Slide 72: Racons
RACON: A radar beacon which produces a coded response or radar paint, when triggered by a radar signal.
Radar transponder beacons
Mounted at center of main channel on some major fixed bridges. Provides enhanced Morse coded echo on radar display.
Will be listed on chart if installed.
Use boat’s radar to verify proper operation of RACON

## Slide 74: Fog Horns
Mounted at center of main channel on some major fixed bridges.
Will be listed on chart if installed.
Normally only sound when fog is present – can only be verified in fog!

## Slide 75: Harlem River – Broadway Bridge

## Slide 76: Harlem River- Spuyten-Duyvil

## Slide 77: Spuyten-Duyvil - tight fit

## Slide 78: Bridge Construction
NAVIGATIONAL CHANNEL THROUGH BRIDGE CONSTRUCTION SITE

## Slide 79: Victory Bridge Demolition

## Slide 80: Victory Center Pier Demo

## Slide 81: Going - Going - Gone!!!

## Slide 82: Obstructions in the Channel
Nothing may be hanging down from the span of the bridge into the navigable channel.
Report any shoaling or other obstructions in the channel.
Is the channel navigable?
Is any debris caught in the fenders sticking into the channel?

## Slide 83: 33CFR117 Subpart A - General Requirements
Subpart A documents the C.G. regulations for operating a drawbridge.
This presentation only shows selected highlights from 33CFR117. The full text is available on line.

## Slide 84: 33CFR117 – Drawbridge Regulations
Sec. 117.5 When the draw shall open.
Except as otherwise required by this subpart, drawbridges shall open promptly and fully for the passage of vessels when a request to open is given in accordance with this subpart.

## Slide 85: 33 CFR 117.9 Delaying the opening of a draw.
No person shall unreasonably delay the opening of a draw after the signals required by Sec. 117.15 have been given.
Note: Trains are usually controlled by the block method. That is, the track is divided into blocks or segments of a mile or more in length. When a train is in a block with a drawbridge, the draw may not be able to open until the train has passed out of the block and the yardmaster or other manager has “unlocked” the drawbridge controls.
The maximum time permitted for delay is defined in Subpart B for each affected bridge. Land and water traffic should pass over or through the draw as soon as possible in order to prevent unnecessary delays in the opening and closure of the draw.
10 minutes is usually considered the maximum time a vessel can be delayed.

## Slide 86: Closing of the draw
Once a vessel has called for an opening, an open bridge may not be closed until that vessel has cleared the bridge.

## Slide 87: 33CFR 117.15 Signals
(a) General.
(1) The operator of each vessel requesting a drawbridge to open shall signal the drawtender and the drawtender shall acknowledge that signal. The signal shall be repeated until acknowledged in some manner by the drawtender before proceeding.
(2) The signals used to request the opening of the draw and to acknowledge that request shall be sound signals, visual signals, or radiotelephone communications described in this subpart.
(3) Any of the means of signaling described in this subpart sufficient to alert the party being signaled may be used.

## Slide 88: 33CFR 117.15 Signals
(b) Sound signals.
(1) Sound signals shall be made by whistle, horn, megaphone, hailer, or other device capable of producing the described signals loud enough to be heard by the drawtender.
(2) As used in this section, “prolonged blast'' means a blast of four to six seconds duration and “short blast'' means a blast of approximately one second duration.
(3) The sound signal to request the opening of a draw is one prolonged blast followed by one short blast sounded not more than three seconds after the prolonged blast. For vessels required to be passed through a draw during a scheduled closure period, the sound signal to request the opening of the draw during that period is five short blasts sounded in rapid succession.

## Slide 89: 33CFR 117.15 Signals
(4) When the draw can be opened immediately, the sound signal to acknowledge a request to open the draw is one prolonged blast followed by one short blast sounded not more than 30 seconds after the requesting signal.
(5) When the draw cannot be opened immediately, or is open and shall be closed promptly, the sound signal to acknowledge a request to open the draw is five short blasts sounded in rapid succession not more than 30 seconds after the vessel's opening signal. The signal shall be repeated until acknowledged in some manner by the requesting vessel.

## Slide 90: 33CFR 117.15 Signals
(d) Radio telephone communications.
(1) Radiotelephones may be used to communicate the same information provided by sound and visual signals. Note: Call signs and radio channels for drawbridges with radiotelephones are listed in Appendix A to this part.
(2) The vessel and the drawtender shall monitor the frequency used until the vessel has cleared the draw.
(3) When radiotelephone contact cannot be initiated or maintained, sound or visual signals under this section shall be used.

## Slide 91: Bridge Operation
Is the draw operational?
Did the bridge tender respond immediately?
If a phone was required, was the phone number correct, and was it answered?
Was the person answering the phone knowledgeable?
Did the horns and alarms on the bridge operate effectively?

## Slide 92: The focus of bridge survey and discrepancy reporting: Prevention Accuracy Credibility Professionalism Service to the Coast Guard.

## Slide 93: The Bridge Program has two components:
Bridge Discrepancy Reports
  Problem reports from any member
Bridge Surveys
  A comprehensive review and report of a bridge done by qualifed Aids Verifiers

## Slide 94: Bridge Survey Report
A detailed review of bridge lights, signs, fenders, gauges & prior discrepancy reports to see if bridge is in compliance with their C.G. bridge permit.
While discrepancies are reported by any member, surveys are done by certified Aids Verifiers.

## Slide 95: Bridge Discrepancies
Allows the staff at the Coast Guard Bridge Branch to contact the bridge owner and get the discrepancy fixed.
Any CGAUX member can file bridge discrepancy reports. Coxswains should keep Bridge Discrepancy forms aboard their facilities.
Report discrepancies within 24 hours of the observation, using your district’s report routing procedure.

## Slide 96: Bridge Discrepancies
Information Needed:
  Any problems on the bridge that affects navigation.
  Any deviation from the CG bridge permit.
Not Needed:
  Non-navigational issues (e.g., bridge condition (except where it affects boats), problems on the bridge roadway.
  Water depths (USACE issue, not bridge office)
  Vertical clearance (unless obstruction is observed).

## Slide 97: Bridge Discrepancies
Survey and discrepancy reporting processes and forms vary by District.
However, information required for reporting is the same as shown on the NS 7055 form (Prevention website).

## Slide 101: Entering observations in the “Discrepancy” section:
Use “Comments” section to accurately describe the problem and where on the bridge it is located. Include digital photos of each discrepancy whenever possible.
Bridge Discrepancy Report

## Slide 102: Bridge Discrepancy Report
Send report, along with digital photos, within 24 hours of observing the discrepancy.
Include digital photos as evidence to support your observations whenever possible – a picture speaks a thousand words!

## Slide 103: Bridge Discrepancy Report
When the CG Bridge Office is alerted of a discrepancy, they send an written order to the bridge owner to repair the deficiency.

## Slide 105: USCG Bridge Letter
An order to the bridge owner to repair the deficiency.
Gives the owner a set time frame to make repairs.
Should be sent back to original observer –
  lets them know their work counted and tells them when to recheck the bridge again.

## Slide 106: Bridge Surveys
Periodic detailed review of lights, signs, fender systems & gauges.
Checks bridge against its USCG permit requirements.
Provides follow up for checking prior reported discrepancies.
Performed by certified Aids Verifiers.

## Slide 107
When you use the term Watching Properly, it is assumed that you did a complete check of the bridge. This usually requires two visits: one during the day at low tide to check e.g. fendering system and gauges, and one at night to check lights.

## Slide 108
Always fill out a complete Light Survey, Fender System Survey, and check the regulatory sign the first time you survey a bridge. Recheck all lights and fenders at each subsequent survey. Recheck gauges & signs at each subsequent survey.

## Slide 109
Reminder…
The Bridge Survey or the Bridge Discrepancy forms get the bridge problem data to the USCG Bridge Branch Office.
You also must report your activity to your IS officer on an ANSC 7030 report (Unit/Individual) to get Auxiliary credit for the work.

## Slide 110
AuxData
AtoN activity (including bridge work) is reported on a 7030 (Unit/Individual)
Never put AtoN activity (missions 30, 31 or 32) on a 7030 (Boat)
Only one person gets 7030 credit for each discrepancy (not all those on the boat)
30 - AtoNs 31- PAtoNs 32 - Bridges

## Slide 111
Bridge Discrepancy Reporting
This Auxiliary program can be quite satisfying, and provides great service to the U. S. Coast Guard and the maritime community.
Our emphasis is on prevention, accuracy, credibility, professionalism and service to the United States Coast Guard

## Slide 112: The End